## Slide 1
Computação Reconfigurável
Aula 2
Valeri Skliarov, Prof. Catedrático
Email: skl@ua.pt
URL: http://sweet.ua.pt/skl/
Departamento de Eletrónica, Telecomunicações e Informática
Universidade de Aveiro
http://elearning.ua.pt/

## Slide 2
Revisão da aula anterior
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
entity TopTrivial is
port ( sw : in std_logic_vector (15 downto 0);
led : out std_logic_vector (15 downto 0));
end TopTrivial;
architecture Behavioral of TopTrivial is
begin
led <= sw;
end Behavioral;
Primeiros passos:

## Slide 3
Aula 2
Síntese e simulação
Tipos de dados, objetos e operadores
Instruções de controlo – decisão: if, when, with, case
Processos combinatórios e sequenciais
VHDL comportamental e estrutural
Exemplos:
  Operações aritméticas
  Processos
  Conversão de tipos
Bibliografia: V.Sklyarov, I.Skliarova, A.Barkalov, L.Titarenko. Synthesis and Optimization of FPGA-Based Systems. Springer, 2014.

## Slide 4
library IEEE;
use IEEE.STD_LOGIC_1164.all;
entity TopTrivial is
port ( sw : in std_logic_vector (15 downto 0);
led : out std_logic_vector (15 downto 0));
end TopTrivial;
architecture Behavioral of TopTrivial is
begin
led <= sw;
end Behavioral;
VHDL (três partes principais)
Três partes principais:
Incluir bibliotecas necessárias
Declarar entidade
Descrever arquitetura
Bibliotecas mais comuns:
library IEEE;
use IEEE.STD_LOGIC_1164.all;
use IEEE.STD_LOGIC_ARITH.all;
use IEEE.STD_LOGIC_UNSIGNED.all;
ou
library IEEE;
use IEEE.std_logic_1164.all;
use IEEE.numeric_std.all;
use IEEE.std_logic_unsigned.all;

## Slide 5
library IEEE;
use IEEE.STD_LOGIC_1164.all;
entity TopTrivialNew is
port ( clk : in std_logic;
sw : in std_logic_vector (15 downto 0);
led : out std_logic_vector (15 downto 0));
end TopTrivialNew;
architecture my of TopTrivialNew is
signal divided_clk : std_logic;
begin
led <= sw when divided_clk = '1' else (others => '0');
div : entity work.clock_divider
port map( clk, '0', divided_clk);
end my;
Frequência do relógio da placa 100 MHz
VHDL:
Comportamental.
Estrutural.
Misto
Declaração de sinais
VHDL (três tipos de descrição principais)

## Slide 6
Declaração de bibliotecas
library . . .
use . . .
Descrição de entidade (interface)
entity <nome de entidade> is
Declaração de parâmetros genéricos – generic
Declaração de portas – port
end <nome de entidade>
library IEEE;
use IEEE.STD_LOGIC_1164.all;
use IEEE.STD_LOGIC_ARITH.all;
use IEEE.STD_LOGIC_UNSIGNED.all;
library IEEE;
use IEEE.std_logic_1164.all;
use IEEE.numeric_std.all;
use IEEE.std_logic_unsigned.all;
Descrição de arquitetura (funcionalidade)
arquitecture <nome de arquitetura > of <nome de entidade> is
Declaração de sinais– signal
Declaração de constantes – constant
Declaração de tipos– type
Declaração de componentes– component
Declaração de funções– function
Declaração de procedimentos– procedure
Declaração de variáveis partilhadas– shared variable
begin
Corpo de arquitetura
end <nome de arquitetura >
entity Counter is
generic (N : integer := 3);
port (
reset : in std_logic;
clk : in std_logic;
My_count: out std_logic_vector(N downto 0)
);
end Counter;
Estrutural
Mista
Comportamental
VHDL (sumário)
parte declarativa de arquitetura
parte declarativa de entidade

## Slide 7
-- comentários até final da linha
Inserir/remover comentários para um conjunto de linhas

## Slide 8
Síntese e simulação
Síntese, implementação e teste
Simulação comportamental
library IEEE;
use IEEE.STD_LOGIC_1164.all;
entity TopTrivial is
port ( sw : in std_logic_vector (15 downto 0);
led : out std_logic_vector (15 downto 0));
end TopTrivial;
architecture Behavioral of TopTrivial is
begin
led <= sw;
end Behavioral;
Geralmente vai precisar de duas partes:
Código VHDL de que queremos simular;
Código VHDL adicional que se chama testbench.
por exemplo:

## Slide 9
Simulação. Exemplo 1.
library IEEE;
use IEEE.STD_LOGIC_1164.all;
entity TopTrivial is
port ( sw : in std_logic_vector (15 downto 0);
led : out std_logic_vector (15 downto 0));
end TopTrivial;
architecture Behavioral of TopTrivial is
begin
led <= sw;
end Behavioral;
library IEEE;
use IEEE.std_logic_1164.all;
entity for_example is
end for_example;
architecture behavior of for_example is
signal sw_in : std_logic_vector (15 downto 0);
signal led_out : std_logic_vector (15 downto 0);
component TopTrivial
port ( sw : in STD_LOGIC_VECTOR (15 downto 0);
led : out STD_LOGIC_VECTOR (15 downto 0));
end component;
begin
uut: TopTrivial
port map (sw => sw_in, led => led_out);
stim_proc: process
begin
sw_in <= (others => '1'); wait for 50 ns;
sw_in <= (others => '1'); wait for 100 ns;
sw_in <= (15 downto 10 => '1', others => '0'); wait for 50 ns;
sw_in <= "1010101010101010"; wait for 70 ns;
sw_in <= (15 downto 13 => '1',10 => '1', 6 downto 5 => '1', others => '0');
end process;
end behavior;
Testbench
1
2

## Slide 10
library IEEE;
use IEEE.STD_LOGIC_1164.all;
entity TopTrivial is
port ( sw : in std_logic_vector (15 downto 0);
led : out std_logic_vector (15 downto 0));
end TopTrivial;
architecture Behavioral of TopTrivial is
begin
led <= sw;
end Behavioral;
library IEEE;
use IEEE.std_logic_1164.all;
entity for_example is
end for_example;
architecture behavior of for_example is
signal sw_in : std_logic_vector (15 downto 0);
signal led_out : std_logic_vector (15 downto 0);
component TopTrivial
port ( sw : in STD_LOGIC_VECTOR (15 downto 0);
led : out STD_LOGIC_VECTOR (15 downto 0));
end component;
begin
uut: TopTrivial
port map (sw => sw_in, led => led_out);
stim_proc: process
begin
sw_in <= (others => '1'); wait for 50 ns;
sw_in <= (others => '1'); wait for 100 ns;
sw_in <= (15 downto 10 => '1', others => '0'); wait for 50 ns;
sw_in <= "1010101010101010"; wait for 70 ns;
sw_in <= (15 downto 13 => '1',10 => '1', 6 downto 5 => '1', others => '0');
end process;
end behavior;
Testbench

## Slide 12
library IEEE;
use IEEE.std_logic_1164.all;
entity for_example is
end for_example;
architecture behavior of for_example is
signal sw_in : std_logic_vector (15 downto 0);
signal led_out : std_logic_vector (15 downto 0);
component TopTrivial
port ( sw : in STD_LOGIC_VECTOR (15 downto 0);
led : out STD_LOGIC_VECTOR (15 downto 0));
end component;
begin
uut: TopTrivial
port map (sw => sw_in, led => led_out);
stim_proc: process
begin
sw_in <= (others => '1'); wait for 50 ns;
sw_in <= (others => '1'); wait for 100 ns;
sw_in <= (15 downto 10 => '1', others => '0'); wait for 50 ns;
sw_in <= "1010101010101010"; wait for 70 ns;
sw_in <= (15 downto 13 => '1',10 => '1', 6 downto 5 => '1', others => '0');
end process;
end behavior;

## Slide 13
library IEEE;
use IEEE.std_logic_1164.all;
library xil_defaultlib;
entity for_example is
end for_example;
architecture behavior of for_example is
signal sw_in : std_logic_vector (15 downto 0);
signal led_out : std_logic_vector (15 downto 0);
component TopTrivial
port ( sw : in STD_LOGIC_VECTOR (15 downto 0);
led : out STD_LOGIC_VECTOR (15 downto 0));
end component;
begin
uut: TopTrivial
uut: entity xil_defaultlib.TopTrivial
port map (sw => sw_in, led => led_out);
stim_proc: process
begin
sw_in <= (others => '1'); wait for 50 ns;
sw_in <= (others => '1'); wait for 100 ns;
sw_in <= (15 downto 10 => '1', others => '0'); wait for 50 ns;
sw_in <= "1010101010101010"; wait for 70 ns;
sw_in <= (15 downto 13 => '1',10 => '1', 6 downto 5 => '1', others => '0');
end process;
end behavior;
Pode alterar o código da seguinte forma:
remover

## Slide 14
Simulação. Exemplo 2 (divisor da frequência).
library IEEE;
use IEEE.STD_LOGIC_1164.all;
use IEEE.STD_LOGIC_ARITH.all;
use IEEE.STD_LOGIC_UNSIGNED.all;
entity clock_divider is
port ( clk, reset : in std_logic;
divided_clk : out std_logic );
end clock_divider;
architecture Behavioral of clock_divider is
signal internal_clock : std_logic_vector (2 downto 0);
begin
process(clk)
begin
if rising_edge(clk) then
if reset = '1' then -- reset sincrono
internal_clock <= (others=>'0');
else internal_clock <= internal_clock+1;
end if;
end if;
end process;
divided_clk <= internal_clock(internal_clock'left);
end Behavioral;
library IEEE;
use IEEE.std_logic_1164.all;
library xil_defaultlib;
entity testbench is
end testbench;
architecture behavior of for_example is
signal clk : std_logic;
signal rst : std_logic;
signal divided_clk : std_logic;
constant clk_period : time := 50 ns;
begin
div: entity xil_defaultlib.clock_divider
port map (clk, rst, divided_clk);
clock_gen process
begin
clk <= ‘0’; wait for clk_period/2;
clk <= ‘1’; wait for clk_period/2;
end process clock_gen;
stim_proc: process
begin
rst <= ‘1’; wait for 30 ns;
rst <= ‘0’; wait for 1000 ns;
end process;
end behavior;

## Slide 16
library IEEE;
use IEEE.STD_LOGIC_1164.all;
use IEEE.numeric_std.all;
use IEEE.std_logic_unsigned.all;
entity Counter is
port (reset : in std_logic;
clk : in std_logic;
My_count : out std_logic_vector(3 downto 0));
end Counter;
architecture Behavioral of Counter is
signal count : std_logic_vector(3 downto 0);
begin
counter: process (clk)
begin
if rising_edge(clk) then
if reset = '1' then
count <= (others => '0');
else count <= count + 1;
end if;
end if;
end process counter;
My_count <= count;
end Behavioral;
library IEEE;
use IEEE.std_logic_1164.all;
library xil_defaultlib;
entity for_example is
end for_example;
architecture behavior of for_example is
signal reset , clk : std_logic := '0';
signal My_count : std_logic_vector(3 downto 0);
constant clk_period : time := 50 ns;
begin
uut: entity xil_defaultlib.Counter
port map (clk, reset, My_count);
clk_generator: process
begin
clk <= '0'; wait for clk_period/2;
clk <= '1'; wait for clk_period/2;
end process clk_generator;
stim_proc: process
begin
reset <= '1'; wait for 50 ns;
reset <= '0'; wait for 100 ns;
reset <= '0'; wait for 100 ns;
reset <= '0'; wait for 100 ns;
reset <= '0'; wait for 500 ns;
end process;
end behavior;
Simulação.
Exemplo 3
(contador).

## Slide 17
Tipos
Tipos de dados, objetos e operadores
Vamos utilizar estes tipos:
Só para simulação
O tipo record é definido por utilizador e permite criar um conjunto de dados dentro de uma estrutura

## Slide 18
Tipos de dados, objetos e operadores
Vamos considerar três tipos de objetos que são:
Sinais (signal) que são declarados na parte declarativa de arquitetura.
Variáveis (variable) que são declaradas na parte declarativa de processo, função e procedimento.
Constantes (constant) que são declaradas na parte declarativa de arquitetura, processo, função e procedimento.
arquitecture <nome de arquitetura > of <nome de entidade> is
Declaração de sinais– signal
begin
Corpo de arquitetura
end <nome de arquitetura >
process (sw)
variable hwc : integer range 0 to 8;
begin
-- . . . . . . . . . . . .
end process;
architecture Behavioral of CombCircuit is
type for_test is array (0 to 3) of std_logic_vector(3 downto 0);
constant for_ex : for_test:=("0001","0010","0100","1000");
begin
-- . . . . . . . . . . . . . . . .

## Slide 19
Tipos de dados, objetos e operadores
aritméticos (arithmetic) (+, -, *, /, abs, mod, rem, sign + and -, **),
concatenação (concatenation) (&),
lógicos (logic) (and, nand, nor, not, or, xnor, xor),
relacionais (relational) (=, /=, <, <=, >, >=),
atribuição (assignment) (:=, <=)
deslocamento (shift) (rol, ror, sla, sll, sra, srl).
Prioridade (precedence) :
(**),
(abs),
(not),
(*),
(/),
(mod, rem),
(+ identity, - negation),
(+,-),
(&),
(rol, ror, sll, srl),
(sla, sra),
(=,/=),
(<, <=, >, >= ),
(and, nand, nor, or, xnor, xor)

## Slide 20
Instruções de controlo – decisão: if, when, with, case .
Processos combinatórios
Circuito combinatório
sw0
sw1
led0
led1
led2
led3
00 0001
01 0010
10 0100
11 1000
Funcionamento
sw0 sw1
led3 led2 led1 led0

## Slide 21
Instruções de controlo – decisão: if, when, with, case .
Processos combinatórios
library IEEE;
use IEEE.STD_LOGIC_1164.all;
entity CombCircuit is
port ( sw : in std_logic_vector (1 downto 0);
led : out std_logic_vector (3 downto 0));
end CombCircuit;
architecture Behavioral of CombCircuit is
begin
led <= "0001" when sw = "00" else
"0010" when sw = "01" else
"0100" when sw = "10" else
"1000" when sw = "11" else "0000";
end Behavioral;
00 0001
01 0010
10 0100
11 1000
Utilizar dentro de arquitetura

## Slide 22
Instruções de controlo – decisão: if, when, with, case .
Processos combinatórios
library IEEE;
use IEEE.STD_LOGIC_1164.all;
entity CombCircuit is
port ( sw : in std_logic_vector (1 downto 0);
led : out std_logic_vector (3 downto 0));
end CombCircuit;
architecture Behavioral of CombCircuit is
begin
with sw select led <= "0001" when "00",
"0010" when "01",
"0100" when "10",
"1000" when "11",
"0000" when others;
end Behavioral;
00 0001
01 0010
10 0100
11 1000
Utilizar dentro de arquitetura

## Slide 23
Instruções de controlo – decisão: if, when, with, case .
Processos combinatórios
library IEEE;
use IEEE.STD_LOGIC_1164.all;
entity CombCircuit is
port ( sw : in std_logic_vector (1 downto 0);
led : out std_logic_vector (3 downto 0));
end CombCircuit;
architecture Behavioral of CombCircuit is
begin
process(sw)
begin
case sw is
when "00" => led <= "0001";
when "01" => led <= "0010";
when "10" => led <= "0100";
when "11" => led <= "1000";
when others => led <= "0000";
end case;
end process;
end Behavioral;
00 0001
01 0010
10 0100
11 1000
Não pode (!!!) utilizar dentro de arquitetura

## Slide 24
Instruções de controlo – decisão: if, when, with, case .
Processos combinatórios
library IEEE;
use IEEE.STD_LOGIC_1164.all;
entity CombCircuit is
port ( sw : in std_logic_vector (1 downto 0);
led : out std_logic_vector (3 downto 0));
end CombCircuit;
architecture Behavioral of CombCircuit is
begin
process(sw)
begin
if sw = "00" then led <= "0001";
elsif sw = "01" then led <= "0010";
elsif sw = "10" then led <= "0100";
elsif sw = "11" then led <= "1000";
else led <= "0000";
end if;
end process;
end Behavioral;
00 0001
01 0010
10 0100
11 1000
Não pode (!!!) utilizar dentro de arquitetura

## Slide 25
Utilização de constantes.
library IEEE;
use IEEE.STD_LOGIC_1164.all;
use IEEE.STD_LOGIC_UNSIGNED.all;
entity CombCircuit is
port ( sw : in std_logic_vector (1 downto 0);
led : out std_logic_vector (3 downto 0));
end CombCircuit;
architecture Behavioral of CombCircuit is
type for_test is array (0 to 3) of std_logic_vector(3 downto 0);
constant for_ex : for_test:=("0001","0010","0100","1000");
begin
led <= for_ex(conv_integer(sw));
end Behavioral;
00 0001
01 0010
10 0100
11 1000

## Slide 26
library IEEE;
use IEEE.STD_LOGIC_1164.all;
use IEEE.STD_LOGIC_UNSIGNED.all;
entity TestCombProc is
port ( sw : in std_logic_vector(7 downto 0);
led : out std_logic_vector(7 downto 0));
end TestCombProc;
architecture Behavioral of TestCombProc is
constant low : integer := 5;
constant high : integer := 10;
begin
process(sw)
begin
if (sw > low) and (sw < high) then led <= sw;
elsif sw < low then led <= not sw;
else led <= (others => '0');
end if;
end process;
end Behavioral;
Processos combinatórios
led <= sw; para valores de interruptores 6,7,8,9 (“0110”, “0111”, “1000”, “1001”).
led <= not sw; para valores de interruptores 0, 1, 2, 3, 4.
Para outros valores de interruptores todos os leds são iguais a 0
Todos os sinais que podem alterar valores dentro do processo devem aparecer na lista de sensibilidade

## Slide 27
Processos sequenciais.
Contador
library IEEE;
use IEEE.STD_LOGIC_1164.all;
use IEEE.STD_LOGIC_UNSIGNED.all;
use IEEE.numeric_std.all;
entity TestSeqProc is
generic ( how_fast : integer := 30);
port ( clk : in std_logic;
sw : in std_logic_vector(15 downto 0);
led : out std_logic_vector(15 downto 0);
btnL : in std_logic;
btnC : in std_logic;
btnR : in std_logic);
end TestSeqProc;
architecture Behavioral of TestSeqProc is
signal internal_clock : unsigned(how_fast downto 0);
signal divided_clk : std_logic;
signal increment : std_logic := btnL;
signal positive_reset : std_logic := btnC;
signal count_enable : std_logic := btnR;
signal count : std_logic_vector(14 downto 0);
begin
led(14 downto 0) <= count;
led(15) <= divided_clk;

## Slide 28
Processos sequenciais.
Contador
sp1: process(clk)
begin
if rising_edge(clk) then internal_clock <= internal_clock+1;
end if;
if falling_edge(clk) then
divided_clk <= internal_clock(internal_clock'left - conv_integer(sw));
end if;
end process sp1;
sp2: process (divided_clk)
begin
if rising_edge(divided_clk) then
if positive_reset = '1' then count <= (others=>'0');
else
if count_enable = '1' then
if increment='0' then count <= count + 1;
else count <= count - 1;
end if;
end if;
end if;
end if;
end process sp2;
end Behavioral;

## Slide 29
Processos sequenciais.
Registo de deslocamento
library IEEE;
use IEEE.STD_LOGIC_1164.all;
use IEEE.STD_LOGIC_UNSIGNED.all;
use IEEE.numeric_std.all;
entity TestSeqProc is
generic ( how_fast : integer := 30);
port ( clk : in std_logic;
sw : in std_logic_vector(15 downto 0);
led : out std_logic_vector(15 downto 0);
btnL : in std_logic;
btnC : in std_logic;
btnR : in std_logic);
end TestSeqProc;
architecture Behavioral of TestSeqProc is
signal internal_clock : unsigned(how_fast downto 0);
signal divided_clk : std_logic;
signal right : std_logic := btnL;
signal positive_reset : std_logic := btnC;
signal load_enable : std_logic := btnR;
signal shift : std_logic_vector(14 downto 0);
begin
led(14 downto 0) <= shift;
led(15) <= divided_clk;

## Slide 30
Processos sequenciais.
Registo de deslocamento
sp1: process(clk)
begin
if rising_edge(clk) then internal_clock <= internal_clock+1;
end if;
if falling_edge(clk) then
divided_clk <= internal_clock(internal_clock'left);
end if;
end process sp1;
sp3: process (divided_clk)
begin
if rising_edge(divided_clk) then
if positive_reset = '1' then shift <= (others=>'0');
else
if load_enable = '1' then shift <= sw;
elsif right = '1' then
shift <= shift(0) & shift(14 downto 1);
else
shift <= shift(13 downto 0) & shift(14);
end if;
end if;
end if;
end process sp3;
end Behavioral;

## Slide 31
VHDL comportamental e estrutural
Descrição do comportamento semelhante à descrição na programação
library ieee;
use ieee.std_logic_1164.all;
entity behavioralVHDL is
port (x1, x2, x3 : in std_logic;
y : out std_logic);
end BehavioralVHDL;
architecture behavioral of BehavioralVHDL is
begin
y <= (x1 and not x2 and not x3) or (not x1 and x2 and not x3) or (not x1 and not x2 and x3);
end behavioral;

## Slide 32
VHDL comportamental e estrutural
Permite descrever um circuito com base em componentes existentes que são incluídos na descrição. Ligações entre componentes são escritas utilizando sinais
Biblioteca Xilinx UNISIM (ficheiro unisim_VCOMP.vhd). Exemplo de descrição:
component AND3B3
port ( O : out std_ulogic;
I0, I1, I2 : in std_ulogic);
end component;
Portos de entrada externos
Porto da saída externo

## Slide 33
VHDL comportamental e estrutural
library ieee;
use ieee.std_logic_1164.all;
library UNISIM;
use UNISIM.Vcomponents.all;
entity StructuralVHDL is
port ( x1,x2,x3 : in std_logic;
y : out std_logic );
end StructuralVHDL;
architecture BEHAVIORAL of StructuralVHDL is
signal out_and1 : std_logic;
signal out_and2 : std_logic;
signal out_and3 : std_logic;
begin
or_circuit : OR3
port map (I0=>out_and1, I1=>out_and2,
I2=>out_and3, O=>y);
and1_circuit : AND3B2
port map (I0=>x3, I1=>x2, I2=>x1, O=>out_and1);
and2_circuit : AND3B2
port map (I0=>x3, I1=>x1, I2=>x2, O=>out_and2);
and3_circuit : AND3B2
port map (I0=>x1, I1=>x2, I2=>x3, O=>out_and3);
end BEHAVIORAL;
Biblioteca Xilinx
begin
or_circuit : OR3
port map (out_and1, out_and2, out_and3,y);
and1_circuit : AND3B2
port map (x3, x2, x1, out_and1);
and2_circuit : AND3B2
port map (x3, x1, x2, out_and2);
and3_circuit : AND3B2
port map (x1, x2, x3, out_and3);
end BEHAVIORAL;
Mapeamento posicional
Mapeamento nomeado
component AND3B3
port (O : out std_ulogic;
I0, I1, I2 : in std_ulogic);
end component;

## Slide 34
VHDL comportamental e estrutural
library IEEE;
use IEEE.std_logic_1164.all;
entity half_adder is
port ( A : in std_logic;
B : in std_logic;
carry_out : out std_logic;
sum : out std_logic);
end half_adder;
architecture half_adder_behavior of half_adder is
begin
sum <= A xor B;
carry_out <= A and B;
end half_adder_behavior;
Half-adder

## Slide 35
VHDL comportamental e estrutural
library IEEE;
use IEEE.std_logic_1164.all;
entity half_adder is
port ( A: in std_logic; B: in std_logic;
carry_out : out std_logic;
sum: out std_logic);
end half_adder;
architecture half_adder_behavior of half_adder is
begin
sum <= A xor B;
carry_out <= A and B;
end half_adder_behavior;
Half-adder (HA)
library IEEE;
use IEEE.std_logic_1164.all;
entity FULLADD is
port ( A, B, carry_in : in std_logic;
sum, carry_out : out std_logic );
end FULLADD;
architecture STRUCT of FULLADD is
signal s1, s2, s3 : std_logic;
component half_adder
port( A,B : in std_logic;
carry_out, sum : out std_logic);
end component;
begin
u1: half_adder port map(A, B, s2, s1); u2: half_adder port map(s1, carry_in, s3, sum);
carry_out <= s2 or s3;
end STRUCT;
Descrição mista

## Slide 36
VHDL comportamental e estrutural
library IEEE;
use IEEE.std_logic_1164.all;
entity half_adder is
port ( A : in std_logic; B : in std_logic;
carry_out : out std_logic;
sum : out std_logic);
end half_adder;
architecture half_adder_behavior of half_adder is
begin
sum <= A xor B;
carry_out <= A and B;
end half_adder_behavior;
Half-adder (HA)
library IEEE;
use IEEE.std_logic_1164.all;
entity FULLADD is
port ( A, B, carry_in : in std_logic;
sum, carry_out : out std_logic );
end FULLADD;
architecture STRUCT of FULLADD is
signal s1, s2, s3 : std_logic;
component half_adder
port( A,B : in std_logic;
carry_out, sum : out std_logic);
end component;
begin
u1: half_adder port map(A, B, s2, s1); u2: half_adder port map(s1, carry_in, s3, sum);
carry_out <= s2 or s3;
end STRUCT;
Descrição mista
entity xil_defaultlib.half_adder
library xil_defaultlib;

## Slide 37
Exemplos: operações aritméticas
Pode criar em Vivado um projeto com base em qualquer projeto existente
Depois pode só alterar código VHDL e modificar o ficheiro XDC

## Slide 38
Exemplos: operações aritméticas
library IEEE;
use IEEE.STD_LOGIC_1164.all;
use IEEE.STD_LOGIC_UNSIGNED.all;
use IEEE.STD_LOGIC_ARITH.all;
entity arith_op is
port ( sw : in std_logic_vector(7 downto 0);
led : out std_logic_vector(8 downto 0);
btnU, btnC, btnD, btnL, btnR : in std_logic);
end arith_op;
-- btnR division; btnL multiplication; btnD addition; btnC subtraction; btnU rest of division
architecture Behavioral of arith_op is
signal result : integer range 0 to 256;
signal but : std_logic_vector(4 downto 0);
begin
but <= btnU & btnC & btnD & btnL & btnR;
result <= 256 when conv_integer(sw(3 downto 0)) = 0 else
conv_integer(sw(7 downto 4)) / conv_integer(sw(3 downto 0))
when but = "00001" else
conv_integer(sw(7 downto 4)) * conv_integer(sw(3 downto 0))
when but = "00010" else
conv_integer(sw(7 downto 4)) + conv_integer(sw(3 downto 0))
when but = "00100" else
conv_integer(sw(7 downto 4)) - conv_integer(sw(3 downto 0))
when but = "01000" else
conv_integer(sw(7 downto 4)) rem conv_integer(sw(3 downto 0))
when but = "10000" else 0;
led(7 downto 0) <= conv_std_logic_vector(result, 8);
end Behavioral;

## Slide 39
Exemplos: operações aritméticas
library IEEE;
use IEEE.STD_LOGIC_1164.all;
use IEEE.STD_LOGIC_UNSIGNED.all;
use IEEE.numeric_std.all; -- use IEEE.STD_LOGIC_ARITH.all;
entity arith_op is
port ( sw : in std_logic_vector(7 downto 0);
led : out std_logic_vector(8 downto 0);
btnU, btnC, btnD, btnL, btnR : in std_logic);
end arith_op;
-- btnR division; btnL multiplication; btnD addition; btnC subtraction; btnU rest of division
architecture Behavioral of arith_op is
signal result : integer range 0 to 256;
signal but : std_logic_vector(4 downto 0);
begin
but <= btnU & btnC & btnD & btnL & btnR;
result <= 256 when conv_integer(sw(3 downto 0)) = 0 else
conv_integer(sw(7 downto 4)) / conv_integer(sw(3 downto 0))
when but = "00001" else
conv_integer(sw(7 downto 4)) * conv_integer(sw(3 downto 0))
when but = "00010" else
conv_integer(sw(7 downto 4)) + conv_integer(sw(3 downto 0))
when but = "00100" else
conv_integer(sw(7 downto 4)) - conv_integer(sw(3 downto 0))
when but = "01000" else
conv_integer(sw(7 downto 4)) rem conv_integer(sw(3 downto 0))
when but = "10000" else 0;
led(7 downto 0) <= std_logic_vector(to_unsigned(result,8)); --led(7 downto 0) <= conv_std_logic_vector(result, 8);
end Behavioral;

## Slide 40
Exemplos: processos
library IEEE;
use IEEE.STD_LOGIC_1164.all;
use IEEE.STD_LOGIC_UNSIGNED.all;
use IEEE.numeric_std.all;
entity arith_op is
port ( sw : in std_logic_vector(7 downto 0);
led : out std_logic_vector(8 downto 0);
btnU, btnC, btnD, btnL, btnR : in std_logic);
end arith_op;
-- btnR division; btnL multiplication; btnD addition; btnC subtraction; btnU rest of division
architecture Behavioral of arith_op is
signal result : integer range 0 to 256;
signal but : std_logic_vector(4 downto 0);
begin
but <= btnU & btnC & btnD & btnL & btnR;
process(but,sw)
begin
if conv_integer(sw(3 downto 0)) /= 0 then
case but is
when "00001" => result <= conv_integer(sw(7 downto 4)) / conv_integer(sw(3 downto 0));
when "00010" => result <= conv_integer(sw(7 downto 4)) * conv_integer(sw(3 downto 0));
when "00100" => result <= conv_integer(sw(7 downto 4)) + conv_integer(sw(3 downto 0));
when "01000" => result <= conv_integer(sw(7 downto 4)) - conv_integer(sw(3 downto 0));
when "10000" => result <= conv_integer(sw(7 downto 4)) rem conv_integer(sw(3 downto 0));
when others => result <= 0;
end case;
else result <= 256;
end if;
end process;
led(7 downto 0) <= std_logic_vector(to_unsigned(result,8));
end Behavioral;
Processo combinatório

## Slide 41
Exemplos: conversão de tipos
signed_vector <= signed(std_logic_vector_signal);
unsigned_vector <= unsigned(std_logic_vector_signal);
std_logic_vector_signal <= std_logic_vector(signed_vector);
std_logic_vector_signal <= std_logic_vector(unsigned_vector);
Seguintes expressões devem utilizar funções de conversão:
integer_signal <= conv_integer (unsigned_vector);
integer_signal <= conv_integer (signed_vector);
integer_signal <= conv_integer (std_logic_vector_signal);
unsigned_vector <= conv_unsigned (integer_signal, size_of_unsigned_vector);
signed_vector <= conv_signed (integer_signal, size_of_signed_vector);
std_logic_vector_signal <= conv_std_logic_vector (integer_signal, size);
use ieee.std_logic_arith.all; → led(7 downto 0) <= conv_std_logic_vector(result, 8);
use ieee.numeric_std.all; → led(7 downto 0) <= std_logic_vector(to_unsigned(result,8));
As funções de conversão são diferentes para pacotes diferentes

## Slide 42
Como encontrar recursos da FPGA utilizados para o seu projeto
1
2
1 CLB = 2 slices.
1 slice = 4 LUTs e 8 flip-flops
LUT – look-up table
I/O – input/output

## Slide 43
FPGA Artix-7 (família 7 de FPGAs de Xilinx)

## Slide 47
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
entity ForSim is
Port ( sw : in STD_LOGIC_VECTOR (15 downto 0);
led : out STD_LOGIC_VECTOR (15 downto 0));
end ForSim;
architecture Behavioral of ForSim is
begin
end Behavioral;

## Slide 48
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
entity ForSim is
Port ( sw : in STD_LOGIC_VECTOR (15 downto 0);
led : out STD_LOGIC_VECTOR (15 downto 0));
end ForSim;
architecture Behavioral of ForSim is
begin
led <= not sw;
end Behavioral;

## Slide 49
library IEEE;
use IEEE.std_logic_1164.all;
library xil_defaultlib;
entity for_example is
end for_example;
architecture behavior of for_example is
signal ssw : STD_LOGIC_VECTOR (15 downto 0);
signal lled : STD_LOGIC_VECTOR (15 downto 0);
-- constant clk_period : time := 50 ns;
begin
uut: entity xil_defaultlib.ForSim
port map (sw=>ssw, led=>lled);
--clk_generator: process
--begin
-- clk <= '0'; wait for clk_period/2;
-- clk <= '1'; wait for clk_period/2;
--end process clk_generator;
stim_proc: process
begin
ssw <= "1111111100000000"; wait for 100 ns;
ssw <= "0101010101010101"; wait for 100 ns;
end process;
end behavior;
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
entity ForSim is
Port ( sw : in STD_LOGIC_VECTOR (15 downto 0);
led : out STD_LOGIC_VECTOR (15 downto 0));
end ForSim;
architecture Behavioral of ForSim is
begin
led <= not sw;
end Behavioral;